## Slide 1: Zeitfrequenzanalyse & Wavelets Dr. sc. nat. Carina Klein FDI: Neuropsychologische Untersuchungsverfahren

## Slide 2: Zeitfrequenzanalyse
Notes: Ganz einfach: filtern

## Slide 3: Zeitfrequenzanalyse: sliding window
Time (s)
www.fieldtriptoolbox.org

## Slide 4: Zeitfrequenzanalyse: sliding window
Time (s)
FFT
Frequency (Hz)
0
high
power
Time (s)
www.fieldtriptoolbox.org
DFT: discrete Fourier Transformation
Notes: Erts wenn Daten komplett isn Fenster passen, wird eine FFT berechnet (power is colour-coded)
Concept:
Here is a signal that is not stationary over time, the amplitude changes over time
Cut signal into snippet
compute power spectrum as a function of frequency, over time
compute Spectral Analysis for each snippet, over time
**window must be filled completed with data, in order to compute the spectrum
Rather than explain power as a line, colour code power as a functoin of frequency on y-axis, time on x-axis
- move on -> get TFR
Highest amplitude oscillation constrained in a particular frequency
Take a snippet of our data, snippet defined by toi
apply a DFT (discrete fourier transform) to compute the spectrum, as a function of frequency
  we then proceed to do this for each snippet, so we are sliding the time window across the entire time range
The representation of the TFR is then a little different from just a spectral representation
  instead of representing power as the vertical axis, and frequency as the horizontal axis
  we represent frequency – vertical time; time = horizontal; power = colour
So here, as we move along the signal, we can see in the TFR that there is an increase in power (Amp^2) in the middle of the signal – constrained at a certain freq range

## Slide 5: Zeitfrequenzanalyse: sliding window
Time (s)
FFT
Frequency (Hz)
0
high
power
Time (s)
Notes: Erts wenn Daten komplett isn Fenster passen, wird eine FFT berechnet (power is colour-coded)
Concept:
Here is a signal that is not stationary over time, the amplitude changes over time
Cut signal into snippet
compute power spectrum as a function of frequency, over time
compute Spectral Analysis for each snippet, over time
**window must be filled completed with data, in order to compute the spectrum
Rather than explain power as a line, colour code power as a functoin of frequency on y-axis, time on x-axis
- move on -> get TFR
Highest amplitude oscillation constrained in a particular frequency
Take a snippet of our data, snippet defined by toi
apply a DFT (discrete fourier transform) to compute the spectrum, as a function of frequency
  we then proceed to do this for each snippet, so we are sliding the time window across the entire time range
The representation of the TFR is then a little different from just a spectral representation
  instead of representing power as the vertical axis, and frequency as the horizontal axis
  we represent frequency – vertical time; time = horizontal; power = colour
So here, as we move along the signal, we can see in the TFR that there is an increase in power (Amp^2) in the middle of the signal – constrained at a certain freq range

## Slide 6: Zeitfrequenzanalyse: sliding window
Time (s)
FFT
Frequency (Hz)
0
high
power
Time (s)
www.fieldtriptoolbox.org
Notes: Erts wenn Daten komplett isn Fenster passen, wird eine FFT berechnet (power is colour-coded)
Concept:
Here is a signal that is not stationary over time, the amplitude changes over time
Cut signal into snippet
compute power spectrum as a function of frequency, over time
compute Spectral Analysis for each snippet, over time
**window must be filled completed with data, in order to compute the spectrum
Rather than explain power as a line, colour code power as a functoin of frequency on y-axis, time on x-axis
- move on -> get TFR
Highest amplitude oscillation constrained in a particular frequency
Take a snippet of our data, snippet defined by toi
apply a DFT (discrete fourier transform) to compute the spectrum, as a function of frequency
  we then proceed to do this for each snippet, so we are sliding the time window across the entire time range
The representation of the TFR is then a little different from just a spectral representation
  instead of representing power as the vertical axis, and frequency as the horizontal axis
  we represent frequency – vertical time; time = horizontal; power = colour
So here, as we move along the signal, we can see in the TFR that there is an increase in power (Amp^2) in the middle of the signal – constrained at a certain freq range

## Slide 7: Zeitfrequenzanalyse: sliding window
Time (s)
FFT
Frequency (Hz)
0
high
power
Time (s)
www.fieldtriptoolbox.org
Notes: Erts wenn Daten komplett isn Fenster passen, wird eine FFT berechnet (power is colour-coded)
Concept:
Here is a signal that is not stationary over time, the amplitude changes over time
Cut signal into snippet
compute power spectrum as a function of frequency, over time
compute Spectral Analysis for each snippet, over time
**window must be filled completed with data, in order to compute the spectrum
Rather than explain power as a line, colour code power as a functoin of frequency on y-axis, time on x-axis
- move on -> get TFR
Highest amplitude oscillation constrained in a particular frequency
Take a snippet of our data, snippet defined by toi
apply a DFT (discrete fourier transform) to compute the spectrum, as a function of frequency
  we then proceed to do this for each snippet, so we are sliding the time window across the entire time range
The representation of the TFR is then a little different from just a spectral representation
  instead of representing power as the vertical axis, and frequency as the horizontal axis
  we represent frequency – vertical time; time = horizontal; power = colour
So here, as we move along the signal, we can see in the TFR that there is an increase in power (Amp^2) in the middle of the signal – constrained at a certain freq range

## Slide 8: Zeitfrequenzanalyse: sliding window
Time (s)
FFT
Frequency (Hz)
0
high
power
Time (s)
…….
www.fieldtriptoolbox.org
Notes: Erts wenn Daten komplett isn Fenster passen, wird eine FFT berechnet (power is colour-coded)
Concept:
Here is a signal that is not stationary over time, the amplitude changes over time
Cut signal into snippet
compute power spectrum as a function of frequency, over time
compute Spectral Analysis for each snippet, over time
**window must be filled completed with data, in order to compute the spectrum
Rather than explain power as a line, colour code power as a functoin of frequency on y-axis, time on x-axis
- move on -> get TFR
Highest amplitude oscillation constrained in a particular frequency
Take a snippet of our data, snippet defined by toi
apply a DFT (discrete fourier transform) to compute the spectrum, as a function of frequency
  we then proceed to do this for each snippet, so we are sliding the time window across the entire time range
The representation of the TFR is then a little different from just a spectral representation
  instead of representing power as the vertical axis, and frequency as the horizontal axis
  we represent frequency – vertical time; time = horizontal; power = colour
So here, as we move along the signal, we can see in the TFR that there is an increase in power (Amp^2) in the middle of the signal – constrained at a certain freq range

## Slide 9: Zeitfrequenzanalyse: sliding window
Time (s)
FFT
Frequency (Hz)
0
high
power
Time (s)
…….
…………….
www.fieldtriptoolbox.org
Notes: Erts wenn Daten komplett isn Fenster passen, wird eine FFT berechnet (power is colour-coded)
Concept:
Here is a signal that is not stationary over time, the amplitude changes over time
Cut signal into snippet
compute power spectrum as a function of frequency, over time
compute Spectral Analysis for each snippet, over time
**window must be filled completed with data, in order to compute the spectrum
Rather than explain power as a line, colour code power as a functoin of frequency on y-axis, time on x-axis
- move on -> get TFR
Highest amplitude oscillation constrained in a particular frequency
Take a snippet of our data, snippet defined by toi
apply a DFT (discrete fourier transform) to compute the spectrum, as a function of frequency
  we then proceed to do this for each snippet, so we are sliding the time window across the entire time range
The representation of the TFR is then a little different from just a spectral representation
  instead of representing power as the vertical axis, and frequency as the horizontal axis
  we represent frequency – vertical time; time = horizontal; power = colour
So here, as we move along the signal, we can see in the TFR that there is an increase in power (Amp^2) in the middle of the signal – constrained at a certain freq range

## Slide 10: Zeitfrequenzanalyse: sliding window
Time (s)
FFT
Frequency (Hz)
0
high
power
Time (s)
…….
…………….
………………………………...
www.fieldtriptoolbox.org
Notes: Erts wenn Daten komplett isn Fenster passen, wird eine FFT berechnet (power is colour-coded)
Concept:
Here is a signal that is not stationary over time, the amplitude changes over time
Cut signal into snippet
compute power spectrum as a function of frequency, over time
compute Spectral Analysis for each snippet, over time
**window must be filled completed with data, in order to compute the spectrum
Rather than explain power as a line, colour code power as a functoin of frequency on y-axis, time on x-axis
- move on -> get TFR
Highest amplitude oscillation constrained in a particular frequency
Take a snippet of our data, snippet defined by toi
apply a DFT (discrete fourier transform) to compute the spectrum, as a function of frequency
  we then proceed to do this for each snippet, so we are sliding the time window across the entire time range
The representation of the TFR is then a little different from just a spectral representation
  instead of representing power as the vertical axis, and frequency as the horizontal axis
  we represent frequency – vertical time; time = horizontal; power = colour
So here, as we move along the signal, we can see in the TFR that there is an increase in power (Amp^2) in the middle of the signal – constrained at a certain freq range

## Slide 11: Evoked vs. Induced activity
Time (s)
Freq (Hz)
Time (s)
Time (s)
www.fieldtriptoolbox.org
Notes: Evoked activity: average over trials to get feature of interest
- Oscillation has same polarity relative to the stimulus each time – you can obtain the feature in the oscillation by averaging
Induced activity: simply averaging does not extract feature because the phases are different/variable across trials
First, we need to compute the

## Slide 12: Verrauschtes Signal -> viele Trials!
Time (s)
Freq (Hz)
www.fieldtriptoolbox.org
Notes: In reality
Noisy single trial
each trial only captures part of the features, but averaging can give the full picture
TF analysis: calculate on single trial level AND THEN average!

## Slide 13: Zeit- vs. Frequenzauflösung
FFT
Frequency (Hz)
Time (s)
www.fieldtriptoolbox.org

## Slide 14: Exkurs: Heisenbergsche Unschärferelation bei Quantenobjekten
Ablenkung der Teilchen im Spalt durch Wirkung des Querimpulses → Ortsbestimmung nach dem Spalt eines Teilchens ist unmöglich
Interferenzmuster
Richtung
Ort
Richtung
Ort
Richtung
Ort
✓
✓
✗
✗
∆x * ∆p = h
Notes: Quantenobjekte: zB Elektron: ist ein Teilchen und eine Welle -> Teilchen hat einen Ort, Welle breitet sich aus und hat damit keinen Ort, aber eine Richtung und eine Geschwindigkeit = Impuls (gibt Geschwindigkeit und Richtung eines Teilchens an)
Durch Beugung breitet sich die Welle hinter dem Spalt (Einzel oder Doppelspalt) in alle Richtungen aus -> Überlagerung der Wellen auf dem Schirm (konstruktive und destruktive Interferenz ((zB Nulllinie wenn Wellen um halbe Wellenlänge zueinander verschoben sind)) lässt das Muster entstehen
Delta x = Ortsunschärfe
Delta p = Impulsunschärfe
H = Planck‘sches Wirkungsquantum (Konstante) => wenn x gross ist, ist y klein und vice versa => nur eine von beiden Eigenschaften ist bestimmbar

## Slide 15: Zeit- vs. Frequenzauflösung
Kurzes Zeitfenster
Langes Zeitfenster
www.fieldtriptoolbox.org
Notes: Be aware of time-frequency tradeoff
Simulated 60 Hz signal
Frequenzauflösung: Relay frequency: 1/legth of time window -> spectral reolution
Increase length of time window -> reduce spectral leakage
Narrow time window = poor frequency resolution -> poor estimate of signal
Large time window = poor temporal resolution -> can’t tell where the effect is
4th window = good
Bottom line: be aware of the values chosen for your foi, toi, and time window; avoid fishing expedition; determine parameters on pilot data

## Slide 16: Wavelet-Analyse
X
=
=
Cosine wave
Taper
Sine wave
www.fieldtriptoolbox.org
Alternative zur Zeit-Frequenzanalyse „sliding window“
Wavelet von franz. ondelette = „kleine Welle“
Abgleich der Waveletfunktion mit den realen Daten
Notes: A wavelet is
Wavelet analysis: convolution (=local correlation) of the eeg signal with a family of waveletswhich capture different frequency components
Taper is applied to the basic functions (sine and cosine waves).
Ondelette franz. Wellchen

## Slide 17: Was ist ein Wavelet?
Frequenz die interessiert
Taper auf Frequenz anwenden
Wavelet
↓
↓
Luck (2005)
Notes: Ein Wavelet pro interessierendem Frequenzband -> Funktion wird getapert (Unterschied zur FFT bei der die Daten getapert werden) -> ergibt Form der Wavelet

## Slide 18: Typische Wavelets

## Slide 19: Wavelets: Zeit- vs. Frequenzauflösung
www.fieldtriptoolbox.org
Notes: Wavelet width determines the time-frequency resolution
Frequency: usually 5 cycles -> are tapered -> stretchend/compress (= temporal resolution) (number of cycles within a wavelet remains the same)
Gaussian taper => Morlet Wavelet (most popular one)

## Slide 20: Wavelets: Zeit- vs. Frequenzauflösung
Waveletlänge (Anzahl Zyklen) ist limitierend für Zeit-/Frequenzauflösung
Tiefe Frequenzen („lange Wavelets“)
    Zeitauflösung ✗
    Frequenzauflösung ✓
Hohe Frequenzen („kurze Wavelets“)
    Zeitauflösung ✓
    Frequenzauflösung ✗
www.fieldtriptoolbox.org
Notes: For Y-axis: specify for which signal you want to ahve an estimate in your freuqency resolution (foi (frequency of interest) & toi (time of interest)) = grid of resolution (for every grid point one value is estimated) -> spectral and temporal smoothing
Division is up to you

## Slide 21: Wavelets
www.fieldtriptoolbox.org
Punktweise Faltung der Waveletfunktion mit den EEG-Daten (pro Frequenz)
Notes: Convolve: point wise correlation
Blue = signal
Red = wavelet
Higher correlation between wavelet and earlier part of signal; low correlation = poor fit

## Slide 22: Literatur
Luck, S.J. (2005) An introduction to the event-related potential technique. MIT Press, 2nd edition. ISBN: 978-0262525855.